## Slide 1: YTP Arduino – Lesson 2
Aug 2018

## Slide 2
Goals
To understand the question “what a micro-controller?”
Learn how to setup an Arduino
Understand Analogue and Digital
Learn how to create the most basic Arduino project
Success Criteria
Setup an Arduino successfully
Complete the Arduino Blink project

## Slide 4
Analogue vs Digital

## Slide 5
Arduino PINS
INPUT
OUTPUT
PINS

## Slide 6
Making ‘sense’ of the World

## Slide 7
Arduino PINS
PINS
INPUT
OUTPUT
40C

## Slide 8
Arduino PINS
INPUT
OUTPUT
40C

## Slide 9
Blink – What you need
2 jumper wires
1 LED
1 220Ω resistor
1 Breadboard
1 Arduino UNO
1 USB cable

## Slide 10
Blink – Building the Circuit

## Slide 11
Blink – Coding the Circuit
Open the Arduino application
Open Blink: File > Examples > 01.Basics > Blink
Plugin your USB cable
Select Arduino UNO in Tools -> Board
Select the port in Tools -> Port
Verify your code
Upload your code

## Slide 12
Extension Activity
1. Swap the resistor for a higher value one
1000Ω
Does anything different happen? Why?
2. Add another blinking LED
What components do you need?
Do you need to use another PIN on the Arduino?
Do you need to write more code?

## Slide 13
Homework
Recap of Arduino hardware and software:
bit.ly/ytp01-led-blink
Using the Arduino Editor
bit.ly/ytp01-the-arduino-editor